## Slide 1: Sleep Conflicts
Andrei Fangli, Adriana Adam

## Slide 2: Smartphone internals (very basics)
A smartphone is made out of a number of devices such as SoC, GPS, Vibrator, Screen and so on
Each device has power states in which they can be found independently from other devices
Each device has a base power state (close to zero battery consumption) and other active power states (that consume more battery).
Each device has a device driver whose code is executed by the CPU
Each device driver controls the power state of its corresponding device

## Slide 3: What is a sleep conflict?
A sleep conflict happens when a device is in a high power state however the SoC is in its base power state (asleep) therefore the CPU cannot execute the driver code that transitions the device in its base power state (close to zero battery consumption)
This means that the device continues to use more power than intended until the CPU can execute the driver code making the transition
To preserve battery, after a brief period of inactivity the SoC enters its base power state meaning that the CPU is asleep and cannot execute any device driver code until it wakes

## Slide 4: What wakes the SoC/CPU?
User interaction with hardware buttons or tapping the screen will wake the SoC
Real Time Clocks which are more like hardware timers can be set and these will wake the SoC
Incoming Phone Calls will wake the SoC
Wake-on-LAN will also wake the SoC
The SoC is a distinct case of device as it can be waken by external events and in turn it can also wake other devices through their driver code that is executed by the CPU

## Slide 5: Sleep conflict, by example
SoC/CPU
3G
Upload this file then turn off
Sure, I’ll transition in the “on state” using driver code executed by the CPU, send the file and then transition in the “off state” using the driver code executed by the CPU.
SoC/CPU
I’m going to sleep now
Anybody home?
Yes, turning off now
turn off (device driver code)
Ok, job’s done, turn me off
3G

## Slide 6: Types of sleep conflicts
Waiting for end of active utilization (waiting for the SoC to wake up)
Waiting for a timeout (after finishing the task the device enters a tail state registering a timer and waiting on that timer to wake the SoC and transition in the suspended state)
Waiting for a program input (application code “instructs” the device to enter a suspended state)
Waiting for external event (devices may be built to allow the wakening of the SoC in some conditions, however the wake may not work rising a sleep conflict)

## Slide 7: HYPNOSIS
A runtime system that performs sleep conflict bug avoidance in smartphones with Android device drivers. A sleep conflict resembles the deadlock problem. In deadlock problems, multiple entities hold some resources while requesting more, and hence none can make progress.
In sleep conflict problems, the CPU and a device are racing to sleep at the moment the device is supposed to be put to sleep. If the CPU sleeps first , it is analogous to holding the resource that the device needs to sleep leading to a deadlock scenario.

## Slide 8: Approaches to find and correct a sleep conflict
The fist approach is a static compiler analysis of each device driver’s code. This approach has two challenges:
First, most device drivers are third-party software and their property code is not available to a static tool;
Second, even if the device driver source code is available, statically analyzing them is extremely difficult because, many device drivers are in a parent-child relationship or because in the low level driver code, there are many functions pointers that are passed between functions and some buses send messages to perform power state transition of the devices.

## Slide 9
The second approach to treating sleep conflicts is avoidance. This is done by checking conditions that can lead to a sleep conflict at every pending system suspension. A major advantage of this approach is that is does not require device driver source code as long as it can monitor power transition. And have access to the FSM power model for each device.

## Slide 10: Design of HYPNOS
HYPNOS provides support for both debugging device drivers before they are deployed, and for catching sleep conflicts in smartphones as they happened, to avoid the power loss resulting from a sleep conflict.
To both detect sleep conflicts before deployment and to avoid sleep conflicts in deployed systems the HYPNOS runtime must check to see if the necessary conditions for a sleep conflict can exist.
That is, at some time when CPU is about to sleep, check firstly if all devices are already in the suspend state and secondly if some are not, determine if their drivers have invoked some mechanism to ensure that the system will wake up at the intended time for the power state transition.

## Slide 11: Sleep conflict testing Methodology
To test all drivers of modern smartphones devices, smartphone devices are grouped into four categories according to how data is being transferred between the device and the CPU. The categories are:
On/Off devices: This category consists of the simplest type of devices such as vibrator, LEDs, and flashlight;
Input devices: This category includes the sensors such as touch-screen, button and accelerometer;
Output device: Speaker is an example for output data device;
Two-way data transfer devices: This category consists of the devices such as SD card, Wi-Fi, 3G, 4G.

## Slide 12: Conclusions
This paper presents the first study of a new class of energy bugs, sleep conflicts, which can occur in smartphone device drivers.
On Android phones, HYPNOS detects several sleep conflict bugs and prevents them from draining the battery. HYPNOS does not require access to driver source code, making it widely applicable.

## Slide 13: Thank You!